## Slide 1: Practical Noise Analysis for 14GHz PLL and Silicon Correlation
Nandu Bhagwan
GHz Circuits, Inc.
WSA: Advances in Noise Analysis for RF Circuits

## Slide 2: Outline
Introduction
Problem Statement
Noise Analysis of a 14GHz PLL
  Compare Different Simulation Methods
  Present Measured Results
  Correlate Silicon to Simulations
Future Advances
Summary

## Slide 3: Introduction
Application: 100Gigabit Ethernet
  Moving from 10G to 100G, 100GBASE-LR4
  Employs OIF-CEI-28G (28 Gbps SERDES)
  Requires Design of High-Speed PLL (28 GHz, effective)
  Requires Stringent Jitter Specifications for PLL (<500fs)
Need to precisely analyze and predict
  PLL Phase noise
  PLL Jitter (Random and Deterministic Jitter)
Need to exploit (or live with) 40nm CMOS and next-generation 28/20/14nm CMOS issues

## Slide 4: Problem Statement
Cost: PLL Simulations are very expensive
  Time
  Compute resources
Breadth: Impossible to do one comprehensive simulation
  To verify phase noise across full spectrum
Creativity: Have to resort to ingenious techniques
  Cannot be ad-hoc, must be structured
  Have to be reliable predictor of Silicon performance

## Slide 5: PLL Blocks & Noise Contribution Characteristics

## Slide 6: Noise Analysis Methods
Architectural Analysis:
  Extract individual parameters and noise contributions of sub-blocks using commercial RF simulators
  Plug these into Architectural Simulator (e.g. TOPS1)
    Frequency Domain
    Time Domain
Transient Noise Analysis:
  Run Transient Noise on full-loop PLL instance
PSS/PNOISE Analysis:
  Run PSS/PNOISE on full-loop PLL instance
1: TOPS is a proprietary GHz Circuits Architectural Simulator

## Slide 7: Noise Analysis Methods: Pros & Cons
Simulation Method | 1 Architectural | 2 Transient Noise | 3 PSS/PNOISE
Effective Analysis Range | Full Band | High Frequency (limited by run time) | Full Band
Spur Evaluation | Freq Domain: No Time Domain: Yes | Yes | No
Noise Modeling of RefClk, Supply, etc. | Yes | No | No
Simulation Setup/Complexity | Simple | Simple | Complex
Convergence Issues | Minimal | None | Possible
Accuracy | Implementation Dependent | Limited by run time (for Low Freq Offsets) | Limited by convergence & Tool issues
Simulation Time | Fast | Long | Moderate to Long, if and after convergence

## Slide 8: Simulation Correlation: Noise Contributor - LPF RZ
Architectural
Transient Noise
Noise floor difference between transient simulation and transient noise simulation
Ignore 1st point in LPHI as calculation artifact
Linearized Verilog-A models, only noise contributor is LPF Rz
Good match validates Architectural Simulator or conversely Transient Noise simulation
Notice difference between numerical noise and small signal random noise – when Transient Noise is turned ON and OFF
Phase Noise dBc/Hz

## Slide 9: Simulation Correlation: Open Loop VCO
Spurs are transformation artifacts, ignore
Good correlation between PSS/PNOISE and Transient Noise
Remember
this hump
 | VCO 1 | VCO 2
VDD | 1.8V | 1.2V
FOUT | 13.7 – 13.8 GHz | 
Conditions | SS, Lo T (0º) | 
Types of Analysis | Transient Noise PSS/PNOISE | 
Phase Noise dBc/Hz

## Slide 10: Simulation Correlation Level Shifters + Quadrature Generator
Circuit scale by 10% removed to deteriorate circuit performance
Good correlation between PSS/PNOISE and Transient Noise
Except for very deteriorated signals at low VCO amplitudes when 1.2V devices are used in level shifter
 | OP Stage 1 | OP Stage 2
Devices used | 1.2V | 0.9 V
VDD | 1V | 
FOUT | 14GHz | 
Conditions | SS, 0.95 V, 0ºC | 
Types of Analysis | Transient Noise PSS/PNOISE | 
0.45V
0.50V
0.55V
Phase Noise dBc/Hz

## Slide 11: Silicon Measurements/ Correlation
Jitter integrated from 1MHz to 3.5GHz
Span of interest for SERDES is 10MHz to 3.5GHz

## Slide 12: Measurements: FF Wafers
Chart: 
Low PLL BW
Medium PLL BW
Higher PLL BW
Phase Noise dBc/Hz
Frequency Offset, Hz

## Slide 13: Measurements: SS Wafers
Chart: 
Low PLL BW
Medium PLL BW
Higher PLL BW
Phase Noise dBc/Hz
Frequency Offset, Hz

## Slide 14: Measurements: Observations
Low Frequency Offsets
  For a clean reference clock, Phase Noise at output improves with increase in BW, even under casual observation
Higher Frequency Offsets
  Differences are not so apparent visually
  Integration BW for this presentation 1M-3.5G
  Actual Requirements 10M-3.5G

## Slide 15: Measurements: Observations
RMS Jitter (fs), ∫1MHz↔3.5GHz, FOUT=7GHz
Spec for this application < 500 fs
FF | Low Amp | Med Amp | Hi Amp
Low BW | 378 |  | 337
Med BW |  | 360 | 
Hi BW | 303 |  | 285
SS | Low Amp | Med Amp | Hi Amp
Low BW | 384 |  | 373
Med BW |  | 366 | 
Hi BW | 333 |  | 307

## Slide 16: Silicon Correlation
Methodology: Pick 2 extremes
  SS wafers, Low Amplitude, Low Bandwidth, worst phase-noise
  FF wafers, High Amplitude, High BW, best phase-noise
Architectural Analysis:
  Frequency Domain Analysis is presented
Transient Noise Analysis:
  Focus should be on higher frequency offsets
PSS/PNOISE Analysis:
  Focus should be on lower frequency offsets if not full band
P

## Slide 17: Silicon Correlation (Best Case) FF Wafers, High BW, High VCO Amp
VCO Dominated
Noise floor of Meas. Eqpt.
Refclk Dominated
FF Wafers
V: 1.2V, 1V
Room Temp
BW ~ 4.2MHz
Amp ~ 0.55V
Fout = 7GHz
Jitter = 285 fs
LEGEND:
LMEAS
LSIM - Total
LSIM – REF
LSIM – VCO
LSIM - OPSTG
Phase Noise dBc/Hz

## Slide 18: Silicon Correlation (Worst Case) SS Wafers, Low BW, Low VCO Amp
VCO Dominated
Output Stages Dominated
Remember this hump ?
Amplitude Modulation
SS Wafers
V: 1.2 V, 1 V
Room Temp
BW ~ 450 KHz
Amp ~ 0.35 V
Fout = 7 GHz
Jitter = 384 fs
LEGEND:
LMEAS
LSIM - Total
LSIM – REF
LSIM – VCO
LSIM - OPSTG
Phase Noise dBc/Hz

## Slide 19: Next Steps
Compare full loop Transient Noise and PSS/PNOISE results with Silicon
Extensions to TOPS
  Frequency domain analysis is currently for LTI 3rd order systems
    Add non-linear, time varying and higher order functionality
  Transient analysis is currently for non-linear time varying and higher order systems
    Add random noise analysis to transient domain simulations

## Slide 20: Summary
Discussed Challenges for 100GBE -SerDes application PLL design
Concentrated on Noise Analysis of the 14GHz PLL
  Compared 3 Different Methods
  Presented Silicon Measurements
  Correlated Silicon Measurements to Simulation Results
Identified important Next Steps